## Slide 1: Sustainability Principles and Practice, 4th ed.
Designing a rainwater harvesting system:
Components

## Slide 2: Rainwater harvesting
Collect rainwater
Store
Use later
City of Austin, Texas Watershed Protection Department

## Slide 3: Rainwater harvesting components:
Catchment area
Conveyance
Filtration
Storage
Distribution
Purification, if for potable use
catchment
1st filtration
storage
nonpotable use
purification
potable use
conveyance
conveyance
distribution
distribution

## Slide 4: Components
US DOE. Rainwater Harvesting Tool

## Slide 5: Catchment: the roof
Ladybird Johnson Wildflower Center Austin, Texas
Smoother is better.
Baked enamel (on steel)
Stainless steel
No zinc, copper, lead
Shingles, shakes, clay tiles more likely to support growth of mold, algae
Treated wood can leach preservatives
Asphalt shingles can leach petroleum compounds

## Slide 6
Ziliker Park Austin, Texas
For small roofs, pipe should store first 5-10 gallons of rainwater
Standpipe
Fills with first flush of rainwater
Once full, remaining water flows to tank
Cleanout plug on bottom
Empty standpipe after each rain event
Filtration – first-flush pipe
City of Austin, Texas Watershed Protection Department

## Slide 7: Conveyance
Ladybird Johnson Wildflower Center Austin, Texas
At least 5”-6” wide
Outer edge of gutter higher than roof side edge
Slope 1/16” to 1/4” per 10 feet of length
Hanger brackets every 30”
From catchment to storage
Gutters:
(From roof to tank)

## Slide 8: Conveyance
3”-4” schedule 40* PVC or PEX
If used for potable water:
  PEX or schedule 40 PVC only (= virgin PVC)
  No drain-waste-vent (DWV) PVC, ABS, copper, galvanized, or lead-containing pipe
VectorMine, Dreamstime
*Schedule 40 refers to wall thickness. Also known as standard pipe.
Zillicker Park
Austin, Texas
Pipe:
(From roof to tank)

## Slide 9
Ladybird Johnson Wildflower Center Austin, Texas
Rain barrel: 55-100 gal
Metal or plastic tank: 200 gal and up
Small system: 1000-1500 gal
Medium system: 5000-10,000 gal
Large system: 10,000-25,000 gal
Very large system: Up to 100,000 gal or more
Storage: barrel, tank, or cistern

## Slide 10: Water is heavy
Tank needs level, compacted base
500 gallons of water = 4170 lb
1000 gallons of water weighs over 4 tons
100 gallons of water = 834 lb
Water weighs 8.34 lb per gallon
  or 62.4 lb per cu ft

## Slide 11: Tank
Tight cover – keep out insects, animals, children
Opaque – if sunlight enters, algae will grow
Optional – inlet from supply system for makeup water
Fully aged water
Aging water
Anaerobic zone
Image courtesy of Texas A&M AgriLife Extension

## Slide 12: Tank
Outlet slope at least 2% for first 5 feet
Overflow maintains maximum high-water line, lets water exit from anaerobic zone.
Screen open end of pipe.
Top 10”-12” of tank is air space
Float with filter
picks up fully aged water
Better for potable use

## Slide 13: Cistern can be underground
Pump required to lift water
US EPA. Semi-Arid Green Infrastructure Toolbox: Rainwater Harvesting

## Slide 14: Simple storage: rain barrel
Screen filters out debris, keeps out mosquitos
Gravity feed to landscape
US EPA. Semi-Arid Green Infrastructure Toolbox: Rainwater Harvesting

## Slide 15: Distribution: gravity or pump
Can be gravity or pump
  Water only flows downhill, unless you pump it.
For every foot of height, water’s weight exerts pressure of 0.43 psi
Water gains 1 psi for every 2.31 feet of height
psi = pounds per square inch
1 ft = 0.43 psi
2 ft = 0.86 psi
3 ft = 1.29 psi

## Slide 16: Distribution: Pump
Reservoir or tank 100 ft above fixture = 0.433 psi x 100 = 43.3 psi
Municipal systems provide 40-80 psi
Plumbing fixtures and drip irrigation systems need at least 20 psi
  For drip systems, unless your tank is 46.5 ft above the lines, you will need a pump.
  Plus you need a filter to avoid clogging drip emitters
US Geological Survey

## Slide 17: Distribution: gravity flow
Rodica Prato, US EPA

## Slide 18: Distribution: gravity flow
You can use hand-held hose from rain barrel
US EPA. Semi-Arid Green Infrastructure Toolbox: Rainwater Harvesting

## Slide 19: Distribution: gravity flow
You can contour soil to direct flow to planting areas, plant basins, rain gardens
Groundwater Foundation
US EPA Watershed Academy

## Slide 20: Potable water:
Drinking water quality
Requires filtration and disinfection systems
Centers for Disease Control

## Slide 21: Purification, if for potable use
Potable: safe for drinking
Regulated by law
Photovs, Dreamstime
Filters
  Sediment filtration (5μ) +
  0.5μ carbon filtration or equivalent
Disinfection, e.g., UV
Buffering for pH control
Backflow prevention
Required:

## Slide 22
Most rainwater systems are for nonpotable water. Use for:
Toilet flushing
Landscape plants
  Do not use on plants that are eaten
  Do not use for washing foods before eating
Rodica Prato, US EPA

## Slide 23: Maintenance
Empty first flush devices after each storm
Keep gutters clean
Trim vegetation at least 24 inches away from gutters
Keep overflow lines free of obstacles that could block flow
Check filters
Check storage tank; flush collected debris at bottom of tank